Firmware Notes
RJ Hegler Technologies, LLC

Project: PostAlert Mailbox

Development Platform: STM32CubeIDE 1.15.1

Processor: STM32C011F6P

PC: Main

Path: C:\Users\Ron\STM32CubeIDE\workspace_1.15.1\STM32C0116_LoRa_Mailbox

Main.c:

/* USER CODE BEGIN Header */
/**
  ******************************************************************************
  * @file : main.c
  * @brief : Main program body
  ******************************************************************************
  * @attention
  *
  * Portions (initialization) Copyright (c) 2024 STMicroelectronics.
  * All rights reserved.
  *
  * This software is licensed under terms that can be found in the LICENSE file
  * in the root directory of this software component.
  * If no LICENSE file comes with this software, it is provided AS-IS.
  *
  * USER Code Copyright (c) 2024 RJ Hegler Technologies, LLC
  ******************************************************************************
  */
/* USER CODE END Header */
/* Includes ------------------------------------------------------------------*/
#include "main.h"
#include "adc.h"
#include "spi.h"
#include "gpio.h"

/* Private includes ----------------------------------------------------------*/
/* USER CODE BEGIN Includes */
#include "LoRa.h"
#include "string.h"
#include "stdio.h"

/* USER CODE END Includes */

/* Private typedef -----------------------------------------------------------*/
/* USER CODE BEGIN PTD */

/* USER CODE END PTD */

/* Private define ------------------------------------------------------------*/
/* USER CODE BEGIN PD */

/* USER CODE END PD */

/* Private macro -------------------------------------------------------------*/
/* USER CODE BEGIN PM */

/* USER CODE END PM */

/* Private variables ---------------------------------------------------------*/

/* USER CODE BEGIN PV */
LoRa myLoRa;
uint16_t LoRa_stat = 0;
uint8_t RxBuffer[20];
uint8_t txpacket[25];
char indata[18];
char TxBuffer[20];
char RxPacket[18];
char BatVolt[12];

uint32_t uid[3];
volatile int tiltBtnISR = 0;
volatile int pairBtnISR = 0;

// Magic numbers for 32-bit hashing. Copied from Murmur3.
static const uint32_t c1 = 0xcc9e2d51;
static const uint32_t c2 = 0x1b873593;
uint8_t mailBoxID[12];
char mbid[11];

uint32_t value_adc;
uint32_t batteryLevel;
char msg[4];
char cw[34] = "(c)2024 RJHegler Technologies, LLC";
char cx[5] = "V1.0";

/* USER CODE END PV */

/* Private function prototypes -----------------------------------------------*/
void SystemClock_Config(void);
/* USER CODE BEGIN PFP */

/* USER CODE END PFP */

/* Private user code ---------------------------------------------------------*/
/* USER CODE BEGIN 0 */
static uint32_t UNALIGNED_LOAD32(const char *p) {
  uint32_t result;
  memcpy(&result, p, sizeof(result));
  return result;
}

static uint32_t Fetch32(const char *p) {
  return UNALIGNED_LOAD32(p);
}

static uint32_t Rotate32(uint32_t val, int shift) {
  // Avoid shifting by 32: doing so yields an undefined result.
  return shift == 0 ? val : ((val >> shift) | (val << (32 - shift)));
}

// A 32-bit to 32-bit integer hash copied from Murmur3.
static uint32_t fmix(uint32_t h)
{
  h ^= h >> 16;
  h *= 0x85ebca6b;
  h ^= h >> 13;
  h *= 0xc2b2ae35;
  h ^= h >> 16;
  return h;
}

static uint32_t Mur(uint32_t a, uint32_t h) {
  // Helper from Murmur3 for combining two 32-bit values.
  a *= c1;
  a = Rotate32(a, 17);
  a *= c2;
  h ^= a;
  h = Rotate32(h, 19);
  return h * 5 + 0xe6546b64;
}

// Generate UID value from uidstr[]

uint32_t Hash32Len5to12(const char *s, size_t len) {
  uint32_t a = (uint32_t)len, b = a * 5, c = 9, d = b;
  a += Fetch32(s);
  b += Fetch32(s + len - 4);
  c += Fetch32(s + ((len >> 1) & 4));
  return fmix(Mur(c, Mur(b, Mur(a, d))));
}

uint32_t map(uint32_t au32_IN, uint32_t au32_INmin, uint32_t au32_INmax, uint32_t au32_OUTmin, uint32_t au32_OUTmax)
{
    return ((((au32_IN - au32_INmin)*(au32_OUTmax - au32_OUTmin))/(au32_INmax - au32_INmin)) + au32_OUTmin);
}

void getBattery(void){
uint32_t voltage;

// get ADC value
 HAL_ADC_Start(&hadc1);
   HAL_ADC_PollForConversion(&hadc1, HAL_MAX_DELAY);
   voltage = HAL_ADC_GetValue(&hadc1);

 // sprintf(msg, "%lu", voltage);

//	float volt = (voltage) * 0.00481;

//	uint16_t volts = volt * 100;

//	sprintf(msg, "%hu", volts);

 if(voltage < 540){voltage = 540;}
 if(voltage > 1034){voltage = 1034;}
 batteryLevel = map(voltage, 540, 1034, 0, 100);

 sprintf(msg, "%lu", batteryLevel);

}
/* USER CODE END 0 */

/**
  * @brief The application entry point.
  * @retval int
  */
int main(void)
{

  /* USER CODE BEGIN 1 */

  /* USER CODE END 1 */

  /* MCU Configuration--------------------------------------------------------*/

  /* Reset of all peripherals, Initializes the Flash interface and the Systick. */
  HAL_Init();

  /* USER CODE BEGIN Init */

  /* USER CODE END Init */

  /* Configure the system clock */
  SystemClock_Config();

  /* USER CODE BEGIN SysInit */

  /* USER CODE END SysInit */

  /* Initialize all configured peripherals */
  MX_GPIO_Init();
  MX_SPI1_Init();
  MX_ADC1_Init();
  /* USER CODE BEGIN 2 */

  HAL_GPIO_WritePin (GPIOB, GPIO_PIN_7, GPIO_PIN_SET);	//PWR_EN -> enable power supply

  myLoRa = newLoRa();

  myLoRa.CS_port = LORA_NSS_GPIO_Port;
  myLoRa.CS_pin = LORA_NSS_Pin;
  myLoRa.reset_port = RST_GPIO_Port;
  myLoRa.reset_pin = RST_Pin;
  myLoRa.DIO0_port = DIO0_GPIO_Port;
  myLoRa.DIO0_pin = DIO0_Pin;
  myLoRa.hSPIx = &hspi1;

  myLoRa.frequency = 915; // default = 433 MHz
  myLoRa.spredingFactor = SF_8; // default = SF_7
  myLoRa.bandWidth = BW_125KHz; // default = BW_125KHz
  myLoRa.crcRate = CR_4_5; // default = CR_4_5
  myLoRa.power = POWER_11db; // default = 20db
  myLoRa.overCurrentProtection = 100; // default = 100 mA
  myLoRa.preamble = 8; // default = 8;

  HAL_Delay(2000);
  // SX1276 compatible module connected to SPI1, NSS pin connected to GPIO with label LORA_NSS
    //uint8_t res = lora_init(&myLoRa, &hspi1, LORA_NSS_GPIO_Port, LORA_NSS_Pin, LORA_BASE_FREQUENCY_US);

  if(LoRa_init(&myLoRa)==LORA_OK){
 LoRa_stat = 1;
  }

  //Receiver side
  LoRa_startReceiving(&myLoRa);

  //uuid code:
  char uidstr[25];
  char uidstr1[7];
  char uidstr2[9];
  char uidstr3[9];
  uint32_t uid;

  // Arrange 12 bytes of UID into uidstr[]
  uid = HAL_GetUIDw0();
  sprintf(uidstr1, "%lu", uid);
//	memcpy (&uidstr[8], &uid, 4);
  uid = HAL_GetUIDw1();
  sprintf(uidstr2, "%lu", uid);

//	memcpy (&uidstr[4], &uid, 4);
  uid = HAL_GetUIDw2();
  sprintf(uidstr3, "%lu", uid);

  strcpy(uidstr, uidstr1);
  strcat(uidstr, uidstr2);
  strcat(uidstr, uidstr3);

  uid = Hash32Len5to12 ((const char *)uidstr, 25);
  sprintf(mbid, "%lu", uid);
  mbid[11] = 0;

 //	tiltBtnISR = 0; //clear isr
 //	pairBtnISR = 0; //clear isr

  /* USER CODE END 2 */

  /* Infinite loop */
  /* USER CODE BEGIN WHILE */
  while (1)
  {

    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

HAL_Delay(500);

 if(tiltBtnISR==1){

 HAL_GPIO_WritePin (GPIOB, GPIO_PIN_7, GPIO_PIN_SET);	//PWR_EN -> enable power supply

 getBattery();

 strcpy(TxBuffer, "md:");
 strcat(TxBuffer, mbid);
 strcat(TxBuffer, ":");
 strcat(TxBuffer, msg);

 memcpy(&txpacket, &TxBuffer, 20);
 LoRa_transmit(&myLoRa, txpacket, sizeof(txpacket), 500);

 // look for ak
 LoRa_startReceiving(&myLoRa);
 uint8_t ct = 0;

 while (HAL_GPIO_ReadPin(GPIOA, DIO0_Pin) == 0 && ct < 10){
HAL_Delay(10);
ct++;
 }
 LoRa_receive(&myLoRa, RxBuffer, 20);	//verify that ak received

//parse data: verify 'ak', skip ':' verify mbid match
 uint8_t i=3;
 uint8_t valid = 0;

 if (RxBuffer[0] != 'a'){
valid = 1;
 }
 if (RxBuffer[1] != 'k'){
 valid = 1;
 }
 while (RxBuffer[i] != ':'){
indata[i-3] = RxBuffer[i];
i++;
 }
 memcpy(&RxPacket, &RxBuffer, 18);
 if (strcmp(indata, mbid) != 0){
 valid = 1;
 }
 if(valid != 0){
 HAL_Delay(100);
 LoRa_transmit(&myLoRa, txpacket, sizeof(txpacket), 500); //retry
 }

 tiltBtnISR = 0; //clear isr
 }

 if(pairBtnISR==1){

 HAL_GPIO_WritePin (GPIOB, GPIO_PIN_7, GPIO_PIN_SET);	//PWR_EN -> enable power supply

 strcpy(TxBuffer, "pr:");
 strcat(TxBuffer, mbid);
 strcat(TxBuffer, ":");
 strcat(TxBuffer, "100");
 memcpy(&txpacket, &TxBuffer, 20);
//	HAL_UART_Transmit(&huart2, txpacket, 20, 1000);
 LoRa_transmit(&myLoRa, txpacket, sizeof(txpacket), 500);
//	LoRa_gotoMode(&myLoRa, SLEEP_MODE);
 while(HAL_GPIO_ReadPin(GPIOA, PAIR_Pin) == 1){
 HAL_Delay(50);
 //***********************need button / door stuck added here
 }
 pairBtnISR = 0; //clear isr
 }

/***************************************************************************
 * keep power on for debugging -> remove commented out for release
 */
 //************************need button / door stuck added here
  HAL_Delay(50);

    uint16_t ct = 0;
  while (HAL_GPIO_ReadPin(GPIOA, TILT_Pin) == 1 && ct < 300){
  HAL_Delay(100);
  ct++;
  }

  if(HAL_GPIO_ReadPin(GPIOA, TILT_Pin) == 1){
  //if (ct > 300){	//if door is open longer than 30 seconds
 strcpy(TxBuffer, "do:");
 strcat(TxBuffer, mbid);
 strcat(TxBuffer, ":");
 strcat(TxBuffer, msg);

 memcpy(&txpacket, &TxBuffer, 20);
 LoRa_transmit(&myLoRa, txpacket, sizeof(txpacket), 500);
  }

 tiltBtnISR = 0; //clear isr
 // everything in deep sleep?
HAL_GPIO_WritePin (GPIOB, GPIO_PIN_7, GPIO_PIN_RESET);	//PWR_EN -> disable power supply

  }
  /* USER CODE END 3 */
}

/**
  * @brief System Clock Configuration
  * @retval None
  */
void SystemClock_Config(void)
{
  RCC_OscInitTypeDef RCC_OscInitStruct = {0};
  RCC_ClkInitTypeDef RCC_ClkInitStruct = {0};

  /** Initializes the RCC Oscillators according to the specified parameters
  * in the RCC_OscInitTypeDef structure.
  */
  RCC_OscInitStruct.OscillatorType = RCC_OSCILLATORTYPE_HSI;
  RCC_OscInitStruct.HSIState = RCC_HSI_ON;
  RCC_OscInitStruct.HSIDiv = RCC_HSI_DIV1;
  RCC_OscInitStruct.HSICalibrationValue = RCC_HSICALIBRATION_DEFAULT;
  if (HAL_RCC_OscConfig(&RCC_OscInitStruct) != HAL_OK)
  {
    Error_Handler();
  }

  /** Initializes the CPU, AHB and APB buses clocks
  */
  RCC_ClkInitStruct.ClockType = RCC_CLOCKTYPE_HCLK|RCC_CLOCKTYPE_SYSCLK
        |RCC_CLOCKTYPE_PCLK1;
  RCC_ClkInitStruct.SYSCLKSource = RCC_SYSCLKSOURCE_HSI;
  RCC_ClkInitStruct.SYSCLKDivider = RCC_SYSCLK_DIV1;
  RCC_ClkInitStruct.AHBCLKDivider = RCC_HCLK_DIV1;
  RCC_ClkInitStruct.APB1CLKDivider = RCC_APB1_DIV2;

  if (HAL_RCC_ClockConfig(&RCC_ClkInitStruct, FLASH_LATENCY_1) != HAL_OK)
  {
    Error_Handler();
  }
}

/* USER CODE BEGIN 4 */
// interrupt entry:
//Receiver side
void HAL_GPIO_EXTI_Falling_Callback(uint16_t GPIO_Pin){

// is irq from tilt sensor?
if(GPIO_Pin == TILT_Pin){
tiltBtnISR = 1;

}
//is irq from pair button?

if(GPIO_Pin == PAIR_Pin){
pairBtnISR = 1;

}else {
//tiltBtnISR = 0;
//pairBtnISR = 0;
     __NOP();
}
}

/* USER CODE END 4 */

/**
  * @brief This function is executed in case of error occurrence.
  * @retval None
  */
void Error_Handler(void)
{
  /* USER CODE BEGIN Error_Handler_Debug */
  /* User can add his own implementation to report the HAL error return state */
  __disable_irq();
  while (1)
  {
 HAL_GPIO_WritePin (GPIOB, GPIO_PIN_7, GPIO_PIN_RESET);	//PWR_EN -> disable power supply
  }
  /* USER CODE END Error_Handler_Debug */
}

#ifdef USE_FULL_ASSERT
/**
  * @brief Reports the name of the source file and the source line number
  * where the assert_param error has occurred.
  * @param file: pointer to the source file name
  * @param line: assert_param error line source number
  * @retval None
  */
void assert_failed(uint8_t *file, uint32_t line)
{
  /* USER CODE BEGIN 6 */
  /* User can add his own implementation to report the file name and line number,
     ex: printf("Wrong parameters value: file %s on line %d\r\n", file, line) */
  /* USER CODE END 6 */
}
#endif /* USE_FULL_ASSERT */